## Slide 1
1
Norwegian experiences with renewable energy
in the district heating sector and industry
International training conference on RES, Gdansk 24-26 November 2015
Financed from Bilateral Cooperation Found EEA Financial Mechanism and Norwegian Financial Mechanism 2009-2014 within the PL04 Operational Programme „Energy saving and promoting renewable energy sources”
Hans Borchsenius
Principal consultant.
Norsk Energi
Hans.borchsenius@energi.no
www.energi.no
Tel +47 22 06 18 00

## Slide 2: Norsk Energi
Industry association established in 1916
80 experts with BSc, MSc and PhD
Consultancy, engineering services, analysis and training
Independent from equipment suppliers and manufactures
90% of turnover from private industry and DH
10 % international projects funded by Norwegian government and International Finance Institutions

## Slide 3
Energy consumption in industry
Renewable energy
63,4 %
Oil, Gas & Coal
36,6 %

## Slide 4: Pulp and paper industry high focus on utilisation of own wood resources
1900 – 1950 Coal
1950 – 1980 Heavy fuel oil
1980  Bioenergy

## Slide 5
Cement Industry
Example: Norcem Brevik
High focus on CO2 reduction
Energy balance (%):
Bioenergy 3
Hydropower 9
Waste 40
Oil 3
Gas 3
Coal 42
Renewable 52
Fossil 48

## Slide 6: Ferroalloy industry High focus on waste heat recovery

## Slide 7
Energy consumption in district heating
Renewable energy
95,7 %
Oil & Gas
4,3 %

## Slide 8: District heating in Europe

## Slide 9: Primary energy supply to district heating in Norway and Poland
Chart: 
| Coal | Oil | Gas | Bio | Other
Poland | 77 | 8 | 5 | 4 | 6
Norway | 0 | 1 | 3 | 20 | 76
%

## Slide 10: Share of renewable energy (%) Depend on energy prices and weather conditions
Chart: 
| 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
 | 86.0552 | 92.2266 | 94.787 | 93.5224 | 96.1205 | 98.5309 | 95.9977 | 98.196 | 98.9057 | 92.6668 | 94.4922 | 76.7338 | 84.3724 | 80.9131 | 76.7013 | 90.1853 | 90.3147 | 83.3821 | 76.3541 | 89.9138 | 92.3774 | 88.581 | 89.143 | 89.7453 | 87.5472 | 81.1607 | 87.9778 | 92.5753 | 94.0719 | 95.6614
 | 13.9448 | 7.7734 | 5.213 | 6.4776 | 3.8795 | 1.4691 | 4.0023 | 1.804 | 1.0943 | 7.3332 | 5.5078 | 23.2662 | 15.6276 | 19.0869 | 23.2987 | 9.8147 | 9.6853 | 16.6179 | 23.6459 | 10.0862 | 7.6226 | 11.419 | 10.857 | 10.2547 | 12.4528 | 18.8393 | 12.0222 | 7.4247 | 5.9281 | 4.3386
Min 76,3 %
Max 98,9 %

## Slide 11: Primary energy supply for district heating in 2014
Chart: 
| Waste combustion | oil | Biofuel | Hydropower | Heat pumps | Gas | Waste heat
 | 1043.2 | 120.5 | 385.9 | 632.9 | 154 | 106.8 | 119.2
The diagram shows country average.
But every city choose local solutions.

## Slide 12: City: Oslo Waste incineration, bio, heat pumps, El
Bioenergy
Heat pumps
Waste
El
Oil Gas

## Slide 13: Klemetsrud Waste Management Plant
Combustion of
  household waste
  industrial waste
  landfill gas
Built in 1983/1986/2010
Annual capacity: 155.000 tonnes of waste
Annual production:
  70 GWhel
  300 GWht

## Slide 14: City: Drammen Heat pump take heat from the sea
Sea water 8  90 degrees Centigrade
Largest ammonia hybrid heat pump in the world
Bioenergy
El
Gas
Heat pump

## Slide 15: City: Porsgrunn Industrial waste heat
99,9 % Waste heat from fertilizer production
0,1 % Gas
Industrial waste heat
Gas

## Slide 16: City: Tønsberg 45 MW woodchip boiler El, oil and gas as peak load
Bioenergy
Oil Gas El

## Slide 17: City: Lillestrøm Bioenergy, Solar heat & heat pump 100 % renewable energy
Bioenergy
Solar heat & heat pump
El

## Slide 18: City: Bodø fuel: Demolition wood
23000 ton demolition wood fuel / year
2x10 MW gas boilers (LPG) as peak load
Heat production = 73 GWh / year

## Slide 19: Low temperature district heating is important for max utilisation of renewable resourses
Development of district heating technology:
1880 First district heating systems introduced in the USA used steam
1930-1970 water > 100 degrees Centigrade
1980 Water 80 degrees Centigrade
2015 Water 40-50 degrees Centigrade
Advantages of low temperature systems:
Reduced heat loss in distribution networks
Possible to utilise low temperature heat sources, like waste heat from industry and buildings, surplus heat from cooling and freezing, solar heating, heat pumps that take heat from the sea, rivers, ground etc.

## Slide 20
CONCLUSION
Norway has the highest share of renewable energy in Europe.
Why:
The electricity sector is almost 100 % based on hydropower
CO2 tax
EU emission trading scheme
Waste policy: Prohibited to put organic waste on landfills (EU waste directive 2009)
DH policy 1: Reduced electricity tax if renewables > 50 %
DH policy 2: Heat consumers may only chose DH or a more environmental friendly alternative.
State investment support to energy efficiency and renewable energy:
  Investment support only to environmental friendly projects
  Size of investment support is about 1 NOK/kWh RES (105 EUR/GWh)
Another reason is also the general public opinion: People WANT to be environmental friendly. The companies WANT to be better than the state regulations require to be attractive to customers.